## Slide 1
CRPA Hardware Architecture
CRPA Hardware Architecture – Interview Assignment
Multi-Band Anti-Jam Antenna Unit for Tactical UAV
Cevat Kaan ERTEN
ROKETSAN, 2026

## Slide 2
Problem Definition & Design Constraints
MISSION
  Tactical UAV platform
  Multi-band GNSS reception
  Anti-jam CRPA processing
  Spatial interference suppression
  Beamformed RF output
  Compatible with existing GNSS receiver
KEY CONSTRAINTS
  8-element reference array
  Array diameter ≤ 35 cm
  Antenna–DACU cable < 60 cm
  DACU mass ≤ 2 kg
  Power ≤ 50 W
  28 V DC supply
  Operating temperature: −40 to +71 °C
  Conduction cooling only
Antenna Array
DACU
GNSS Receiver

## Slide 3
CRPA Operating Principle
How it works :
  Multiple antenna elements receive the same signals with different phase relationships
  Each channel is multiplied by a complex weight
  Weighted signals are coherently combined
  Interference is cancelled in selected spatial directions
  GNSS signals from other directions are preserved as much as possible
X
Complex Weights
w1,w2,w3,...,w8
Weighted Combination
y(t) = Σ wₙxₙ(t)
Beamformed RF Output
(Interference-Suppressed RF Output)

## Slide 4
Group | System | Center Frequencies [MHz] | Signals | Required RF Coverage | Main-Lobe BW [MHz]
L1 | GPS, Galileo, BeiDou, GLONASS | 1575.420, 1575.420, 1561.098, 1602+k·0.5625 | L1 C/A, E1 OS, B1I, G1 C/A | 1559.052–1605.886 MHz | 2.046 / 14.322 / 4.092 / 1.022
L2 | GPS, Galileo, BeiDou, GLONASS | 1227.600, 1207.140, 1207.140, 1246+k·0.4375 | L2C, E5b, B2I, G2 C/A | 1196.910–1249.136 MHz | 2.046 / 20.460 / 4.092 / 1.022
L5 | GPS, Galileo, BeiDou | 1176.450 | L5, E5a, B2a | 1166.220–1186.680 MHz | 20.460
GNSS Signals & Frequency Coverage
Target Signal Groups and Required RF Coverage
L2 BAND
52.226 MHz
Required RF Coverage
L5 BAND
20.460 MHz
Required RF Coverage
L1 BAND
46.834 MHz
Required RF Coverage
GNSS Signal Structure:
RF Carrier + PRN Spreading Code + Navigation Data
RF Carrier:
defines the center RF frequency of the signal
Spreading Code:
spreads the signal spectrum; chip rate and modulation determine the useful bandwidth
Typical Received Level:
≈ −130 dBm at receiver input

## Slide 5
Preliminary Frequency Plan
CHAIN 1 — L1
CHAIN 2 — L5 + L2
1559.052 MHz ─────────●───────── 1605.886 MHz
LO: 1582.469 MHz
BW: 46.834 MHz
Baseband: ±23.417 MHz
Sampling: 76.8 MS/s
1166.220 MHz ─────────●───────── 1249.136 MHz
LO: 1207.678 MHz
BW: 82.916 MHz
Baseband: ±41.458 MHz
Sampling: 122.88 MS/s
OPTIONAL — Galileo E5 AltBOC Alternative
E5a E5 Center E5b
1176.450 MHz 1191.795 MHz 1207.140 MHz
●----------------------●----------------------●
15.345 MHz 15.345 MHz
  E5a and E5b are already captured within Chain 2;
AltBOC treats them jointly as one wideband Galileo E5 signal.
  AltBOC-oriented alternative: Chain 1: L1 | Chain 2: E5 wideband | Chain 3: Upper L2

## Slide 6
Optional AltBOC-Oriented Frequency Plan
CHAIN 1 — L1
RF Range
1559.052 – 1605.886 MHz
BW: 46.834 MHz
LO: 1582.469 MHz
1559.052 MHz ───── ● ───── 1605.886 MHz
LO₁
CHAIN 2 — E5 WIDEBAND
RF Range
1166.220 – 1217.370 MHz
BW: 51.150 MHz
LO / E5 Center: 1191.795 MHz
1166.220 MHz ───── ● ───── 1217.370 MHz
LO₂
CHAIN 3 — UPPER L2
(GPS L2C + GLONASS G2)
RF Range
1226.577 – 1249.136 MHz
BW: 22.559 MHz
LO: 1237.857 MHz
1226.577 MHz ───── ● ───── 1249.136 MHz
LO₃
1226.577 MHz
1237.857 MHz
1249.136 MHz
LO₃
(Chain 3)
LO₂
(Chain 2 - E5 AltBOC)
1166.220 MHz
1191.795 MHz
1217.370 MHz
1559.052 MHz
1582.469 MHz
1605.886 MHz
LO₁
(Chain 1)
Image Band about LO (Chain 2)
Image Band about LO (Chain 3)
Image Band about LO (Chain 1)
1191.795 MHz
LO₂
2383.590 MHz
2LO₂
3575.385 MHz
3LO₂
1237.857 MHz
LO₃
2475.714 MHz
2LO₃
3713.571 MHz
3LO₃
1582.469 MHz
LO₁
3164.938 MHz
2LO₁
4747.407 MHz
3LO₁
Image & LO Harmonic Locations

## Slide 7
Criterion | Zero-IF RFIC | Direct RF Sampling
Performance | Complex I/Q output; suitable for phase-coherent CRPA processing. Requires I/Q calibration. | Avoids analog I/Q conversion; high dynamic range possible, but ADC jitter and blocker handling are critical.
Component Count | High integration: mixers, LO/PLL, VGA and ADC may be integrated. | Simpler analog path, but requires high-speed ADC and heavier digital processing.
Power | Lower sampling-rate and digital-processing demand. | Higher ADC and FPGA power due to direct RF sampling.
Mass / Size | Compact RFIC-based implementation. | ADC, clocking and digital hardware can increase PCB area and thermal load.
Cost | Typically lower for a replicated multi-channel system. | High-speed ADC and FPGA resources increase cost.
Design Ease | Easier data-rate management; DC offset, LO leakage and I/Q mismatch must be handled. | Analog chain is simpler, but clocking, ADC interface and FPGA DDC are more demanding.
Receiver Architecture Comparison
Zero-IF RFIC vs. Direct RF Sampling :
SELECTED ARCHITECTURE :
ZERO-IF RFIC
  Lower ADC sampling rate
  Lower data throughput
  Lower power / SWaP
  Native complex I/Q output
Trade-offs
  I/Q mismatch
  DC offset
  LO leakage
  More analog/RF functional complexity

## Slide 8
Zero-IF CRPA Receiver Block Diagram
8-Element CRPA Antenna Array
Passive Tri-Band L1/L2/L5 Patch Elements
RF Front-End
Preselector Filter + LNA
Zero-IF Receiver (RFIC / ADC)
I/Q Downconversion + Baseband Filtering + ADC
FPGA Processing
Channel Alignment + Calibration + Complex Weighting + Summation
RF Output Chain
DAC + Upconversion + RF Output
Existing GNSS Receiver
Existing onboard receiver — no modification required
Reference Clock & Distribution
Common Frequency Reference

## Slide 9
Antenna-Side vs. DACU Component Placement
ANTENNA-Side
DACU
• LNA Stage :
Placed close to each antenna element to minimize pre-LNA cable loss and preserve system noise figure.
• Preselector Filter :
Placed close to the receiver to suppress out-of-band blockers before the RFIC.
• Zero-IF RFIC / ADC :
Performs I/Q downconversion, baseband filtering and digitization for each receive channel.
• FPGA Processing :
Performs channel alignment, calibration, complex weighting and summation for CRPA processing.
• Reference Clock & Distribution :
Provides a common frequency/time reference to maintain phase coherence across all receive channels.
• RF Output Chain :
Converts the processed digital/baseband signal back to RF and feeds the existing GNSS receiver.
• Passive Tri-Band Patch Antenna :
Receives L1/L2/L5 GNSS signals from each array element.
Design Constraint: Antenna-to-DACU RF interconnect < 60 cm per element.

## Slide 10
Elements | RF Chains | RFIC / ADC Qty | Est. Power | Raw I/Q Data Rate | Est. DACU Mass | Budget
4 | 8 | 2 | ~22 W | 25.56 Gb/s | ~0.8 kg | PASS
8 | 16 | 4 | ~31.35 W | 51.12 Gb/s | ~1.1 kg | PASS
12 | 24 | 6 | ~47.7 W | 76.68 Gb/s | ~1.4 kg | PASS
16 | 32 | 8 | ~64.9 W | 102.24 Gb/s | ~1.7 kg | FAIL — Power
Array Geometry & System Scaling
Selected Geometry: 8-Element Uniform Circular Array (UCA)
fmax = 1605.9 MHz
λmin = c / fmax
λmin = 3×10⁸ / 1.6059×10⁹ ≈ 0.1868 m = 18.68 cm
  Design Wavelength at L1 Upper Edge :
  Element Spacing :
D = d / sin(π / N)
D = 9.34cm / sin(22.5°) ≈ 24.4cm
N = 8
d / λmin = 9.34 / 18.68 = 0.5
L1 wavelength: λmin ≈ 18.68 cm
Nearest-neighbor spacing: d ≈ 9.34 cm
Pitch-Circle Diameter: D ≈ 24.4 cm
Baseline Components Used for Scaling
  RFIC / ADC: Analog Devices ADRV9026
  FPGA: AMD Kintex UltraScale+ XQKU5P
  LNA: Analog Devices ADL5521
  Clock Distribution: Analog Devices HMC7044B
  Reference Oscillator: SiTime SiT9346
  L1 Preselector Filter: Anatech AM1600S1059
  L2 + L5 Preselector Filter: Abracon AFII-SW-0065

## Slide 11
Source | Freq. | EIRP | Gant | Distance | FSPL | Prx
J1 - CW jammer | 1575.42 MHz | 50 dBm | −15 dBic | 5 km | 110.4 dB | −75.4 dBm
J2 - Noise Jammer | 1176.45 MHz | 50 dBm | −12 dBic | 8 km | 111.9 dB | −73.9 dBm
J3 - | 1486 MHz | 60 dBm | −18 dBic | 4 km | 107.9 dB | −65.9 dBm
Source | In-band / Out-of-band | Suppression Method | Reason
J1 - CW jammer | In-band L1 | Spatial nulling | Same band as desired L1 GNSS
J2 - Noise Jammer | In-band L5 | Spatial nulling | Same band as desired L5 GNSS
J3 | Out-of-band | Preselector filtering | Outside desired GNSS bands
Interference Power & Suppression Strategy
FSPL = 32.44 + 20log10(dkm) + 20log10(fMHz)
  Representative GPS Signal Levels
L1 C/A ≈ −128.5 dBm
L2C ≈ −130.0 dBm
L5 ≈ −127.9 dBm
  Thermal Noise Floor
L1 chain (46.834 MHz) ≈ −97.3 dBm
L2+L5 chain (82.916 MHz) ≈ −94.8 dBm
  Jammer Severity
J1: −75.4 dBm → ≈53.1 dB above GPS L1 C/A reference level
J2: −73.9 dBm → ≈54.0 dB above GPS L5 reference level
J3: −65.9 dBm → strongest received interferer; out-of-band with respect to the desired GNSS bands
  J3 Preselector Requirement
J3 received power: −65.9 dBm
Target residual: ≤ L1 thermal-noise floor
Required rejection: ≈ 31.4 dB
Design target: ≥ 32 dB at 1486 MHz

## Slide 12
Stage | Gain / Loss* | NF* | Linearity / Limit
ADL5521 LNA | +13 / +15 dB | ≈1.0 dB | OP1dB ≈ +21.8 dBm
GNSS Diplexer | −1.0 dB | ≈1.0 dB | +30 dBm CW
Preselector | −4.0 / −1.2 dB | 4.0 / 1.2 dB | Passive
ADRV9026 Rx | Variable | ≈11.5 dB | IIP3 > +15 dBm
RF Front-End, Cascade & ADC Headroom
Selected RF Front-End :
Antenna
ADL5521 LNA
Johanson 1224DP15A1572001E
Diplexer
ADRV9026
AM1600S1059
(L1 Filter)
ADRV9026
AFII-SW-0065
(L2+L5 Filter)
L1 Filter — AM1600S1059 :
Passband: 1550–1650 MHz
Insertion Loss: ≤ 4.0 dB
Rejection: ≥ 45 dB at 1200–1500 MHz
L2+L5 Filter — AFII-SW-0065 :
Passband: 1166–1300 MHz
Insertion Loss: 1.0 dB typ. / 1.9 dB max
Rejection: ≥35 dB at 1400–1520 MHz
Selected order: LNA → Diplexer → Filter
Reason: Avoids pre-LNA insertion loss and preserves receiver noise figure.
Friis: F_total = F_1 + (F_2-1)/G_1 + (F_3-1)/(G_1 G_2) + (F_4-1)/(G_1 G_2 G_3)
GNSS Diplexer — Johanson 1224DP15A1572001E :
Low band: 1164–1285 MHz
High band: 1539–1606 MHz
IL ≤ 1.0 dB
Values are given as L1 / L2+L5 where applicable.
Cascade Noise Figure
  L1: ≈ 5.4 dB
  L2+L5: ≈ 2.9 dB
  L1: Total Rx input ≈ −67.0 dBm → ≈56.3 dB headroom
ADC Full-Scale Headroom
  L2+L5: Total Rx input ≈ −60.8 dBm → ≈50.1 dB headroom
Total Noise Figure: NF_total = 10 log_10(F_total)
Input-referred headroom using ADRV9026 P_HIGH= -10.7 dBm

## Slide 13
ADRV9026 #1
Amplitude Error [dB] | Phase Error [°] | Null Depth Limit [dB]
0.5 | 5 | −19.5 dB
0.2 | 2 | −27.5 dB
0.1 | 1 | −33.6 dB
0.05 | 0.5 | −39.6 dB
ADRV9026 #2
DEVCLK + SYSREF
SiT9366
122.88 MHz Master Reference
HMC7044B
Clock / SYSREF Distribution
ADRV9026 #3
ADRV9026 #4
FPGA
JESD204C High-Speed Serial Links
DAC
Upconverter
RF Output
Existing GNSS Receiver
Calibration injection before LNA, common signal distributed to all 8 channels
Data Interface :
  8 antenna elements
  L1 sampling rate: 76.8 MSPS
  L2+L5 sampling rate:
  122.88 MSPS
  ADC output: 16-bit I + 16-bit Q = 32 bits/sample
R_total = 8 × (76.8 + 122.88) × 10^6 × 32 ≈ 51.12 Gb/s
Selected interface: JESD204C
Reason: Native ADRV9026 support, lower 64b/66b overhead, and sufficient lane-rate margin.
FPGA Selection :
AMD Kintex UltraScale+ XQKU5P
  16 × GTY transceivers — up to 28.2 Gb/s
  1824 DSP slices
  ~34 Mb on-chip memory
  Supports the required JESD204C throughput
  27 × 27 mm package
  Selected for high-speed interface capability, power efficiency, and compact size
Calibration Source
1-to-8 Distribution
Injection Before LNA
8 RF Channels
Synchronization :
Calibration :

## Slide 14
Component | Part Number | Quantity | Availability Status | Approximate Unit Price
LNA | ADL5521ACPZ-R7 | 8 | Active | ≈ $5.43
L1 Filter | AM1600S1059 | 8 | Active | RFQ
L2/L5 Filter | AFII-SW-0065-T | 8 | Active | ≈ $2.64
RFIC / ADC | ADRV9026BBCZ | 4 | Active | ≈ $1,409
FPGA | XQKU5P-1FFRB676I | 1 | Active | ≈ $4,000
Reference Oscillator | SiT9366 (122.88 MHz) | 1 | Active | ≈ $25
Thermal Phase Stability & BOM / SWaP-C
Temperature-Induced Phase Drift
  Temperature changes cause channel-to-channel phase drift in RF/PCB paths.
  Phase mismatch reduces achievable null depth.
  Periodic calibration updates the channel phase-correction coefficients.
Critical Component BOM Summary
Power Budget :
  4 × ADRV9026: 16.76 W
  8 × ADL5521: 2.40 W
  XQKU5P FPGA: ~10.0 W
  HMC7044B: 1.93 W
  SiT9366: 0.26 W
  DAC + Upconverter reserve: ~2.0 W
  Electronics subtotal: ~33.4 W
  Estimated total power: ~40 W
  Requirement: ≤ 50 W
  Power margin: ~10 W
Mass Budget :
  PCB + electronics: ~0.35 kg
  Aluminum enclosure + baseplate: ~0.75 kg
  Connectors + shielding + wiring: ~0.20 kg
  Mechanical hardware: ~0.10 kg
  Engineering reserve: ~0.20 kg
  Estimated total mass: ~1.60 kg
  Requirement: ≤ 2.0 kg
  Mass margin: ~0.40 kg
Main cost drivers: ADRV9026 RFICs and the XQKU5P FPGA, due to their much higher unit cost than the remaining RF components.
Supply risk: ADRV9026 and XQKU5P are high-cost, specialized components; AM1600S1059 has limited sourcing.
Alternatives: ADRV9026 → TI AFE7950; XQKU5P → XCKU5P-2FFVB676I; AM1600S1059 → EMA4F1580P80G30B

## Slide 15
References
  E. D. Kaplan and C. J. Hegarty, Understanding GPS/GNSS: Principles and Applications, 3rd ed., Artech House.
  B. Razavi, RF Microelectronics, 2nd ed., Pearson.
  D. M. Pozar, Microwave Engineering, 4th ed., Wiley.
  U.S. Space Force, IS-GPS-200N – Navstar GPS Space Segment / Navigation User Interfaces.
  U.S. Space Force, IS-GPS-705J – GPS L5 Interfaces.
  European Union / EUSPA, Galileo Open Service Signal-In-Space ICD.
  China Satellite Navigation Office, BeiDou Open-Service SIS ICDs.
  GLONASS, Interface Control Document – Open Service Navigation Signals in L1/L2.
  Analog Devices, ADL5521 Low Noise Amplifier Data Sheet.
  Johanson Technology, 1224DP15A1572001E GNSS Diplexer Data Sheet.
  Anatech Electronics, AM1600S1059 SAW Band-Pass Filter Data Sheet.
  Abracon, AFII-SW-0065 Multi-Band GNSS Filter Product Specification.
  Analog Devices, ADRV9026 Integrated Quad RF Transceiver Data Sheet.
  Analog Devices, ADRV9026 FAQ / EngineerZone – Rx ADC Resolution and SFDR.
  Analog Devices, HMC7044B Clock Generator / Jitter Attenuator Data Sheet.
  SiTime, SiT9366 Ultra-Low-Jitter Differential Oscillator Data Sheet.
  AMD, Kintex UltraScale+ XQ / XQKU5P Device Documentation.
  Texas Instruments, AFE7950 RF-Sampling Transceiver Documentation.
  Echo Microwave, EMA4F1580P80G30B Filter Specification.
  Manufacturer/distributor web listings (DigiKey, Avnet, Analog Devices, AMD, SiTime, Anatech, Abracon), accessed Oct. 2026, for approximate pricing and availability.